## Slide 1
09.10.2017
Android Auto
Notes: Good morning, thank you all for you presence, my name is João Ramos and this is Mauro Pires, and we are going to make a presentation about Android Auto

## Slide 2: Agenda
1
Overview - Android Auto
2
How it works?
3
Building Apps for Auto
4
Compatible with Android Auto
5
Embedded Android Auto
Notes: We divide the presentation in 5 sections, in the first we will give you an overview about Android Auto, after that we are going to explain how it works. In the third section we are going to explain how to build an app for Auto and some resterictions associated in the building process. In the forth section we will present some car and aftermarket displays, that have already implemented Android Auto, and also some countries which the application is available. Finally we are going to talk about Embedded Android Auto, which was presented in google I/O 2017

## Slide 3: 1.
Overview- Android Auto

## Slide 4: Overview- Android Auto
Release Date: March 19, 2015
Android Application for smartphone that allows a connection with the car using a USB cable
Android Auto connects via Bluetooth, in order to connect with the car sound system
Simpler is safest
  Only brings useful information
  Organized into simple cards
  Apps need to have consistent design
        Large and round buttons, for easy touch points
        Similar menu structures

## Slide 5: Comparison with Competitor Technologies
GPS Navigation
  Google maps is the more precise and user friendly application for GPS Navigation
Voice Control
  Speech recognition from Google is more refined, and his able to interpret more commands
Not compatible car
  Android Auto has the ability to work in the phone
Notes: The biggest advantage to use Android Auto instead of the implemented IVI (in vehicle infotainment) of a brand, is that using android Auto we get updates from google, however in a implemented IVI, once is done is done, there are no updates.
We know there are people who prefer using other apps for GPS Navigation, but in most of the videos and reviews we saw, they say that Google Maps is the best for being more precise and user friendly, than the others
We saw the comparison between voice control system between google and Apple, and the google voice control performs better, in the interpretation of what a person wants to say.
We also don’t need to buy a new car or spend 700€ in a aftermarket display, we can simply use our phone to do the work.

## Slide 6: 2.
How it works?

## Slide 7: How it works?
If connected to the car the phone stays unusable
There are 5 panels available, if connected with the car dash screen
  If we use the phone there are 4 panels available
    Home menu has information such as the weather, current song, current destination and upcoming appointments
    Only important information appear while driving
      Notifications such as alerts from Email, Facebook or Twitter, will not show in the notifications log
Notes: Need to be android 5.0 plus
5 panels -> navigation, phone log, home, media, car diagnosis
Important information, like a message received, from whatsupp, facebook messeger or hangouts
A phone call incoming

## Slide 8: Voice Command
To start Voice Command we can use:
  At the beginning of the sentence we say “OK Google”
  By a button placed in the top right corner
  Press the talk button presented in steering wheel
Using Voice Command we can:
  Set the destination place
  Call a person
  Initialize a song
  Access to any menu
Notes: Like said before, the car sound system is connected via bluethoot.
We have a lot of options to start a voice command, for example if we use the “OK Google”, we don’t need to touch the screen, and keep the eyes on the road at the same time we are doing something else.
A example to set the destination we can say “OK Google, set directions to …” and we say the address.
We can also ask for a specific song in a specific app
Basically, We can use every OK Google command available for android system

## Slide 9: Android Auto - Panels
On phone Screen
On Car Dash Screen
Notes: Here is shown the phone screen and the car dash screen, and the blue markers show the panel with 5 or 4 buttons
For car diagnosis the app called Torque is the one that is used

## Slide 10: Android Auto - Home Menu
On phone Screen
On Car Dash Screen
Notes: Here is shown some examples of the home menu, where we see the relevant information, in the case of the phone we see the current destination, the actual music and a received message, in the car dash is shown a received message, a coming appointment and the current wheather

## Slide 11
When a message is received

## Slide 12: 3.
Building Apps for Auto

## Slide 13: Set up an Auto project
Auto supports two types of apps
Audio apps - allow users to browse and play music and spoken audio
Messaging apps - receive incoming notifications, read message via text-to-speech, and send replies via voice input
Prerequisites
Create or update your app project - target Android 5.0 (API level 21) or higher
Install the support library- NotificationCompat.CarExtender class allows you to create notifications that are compatible with Auto devices
Declare Auto capabilities
Define the Auto XML configuration- Specify the car capabilities that your app uses in an XML file
Add a manifest entry - provide a reference to the Auto XML configuration file you created
Add Auto features to your apps
Notes: https://developer.android.com/training/auto/start/index.html#dev-project

## Slide 14: Providing Audio Playback for Auto
Build a Browser Service
Media browser service extends MediaBrowserService class
Android Auto includes a browsing capability that lets users select a letter from an on-screen keyboard
Building content hierarchy
Enable Playback Control
Register a media session - set a callback object that is used to handle playback control requests
Implement play commands - your app must extend the abstract MediaSession.Callback class and implement the methods that your app supports
    Support Voice Actions
Enable your audio app to launch with a voice command - "Play [search query] on [your app name]"
Parse the voice query to build the playback queue
Playback control actions - implement the callback methods with the playback controls that you support in your app.
Notes: Android Auto can contact your service to do the following:

## Slide 15: Providing Messaging for Auto
Define read and reply intent filters
Define the read action and reply action intent types for your app and the BroadcastReceiver classes
Import Support Library for Messaging
Update the support libraries, building notifications requires classes from the v4 support library
Notify Users of Messages
Create conversation read and reply intents - create a PendingIntent object for each of these actions
Set up the conversation builder - Auto organize messages into conversations
Handle User Actions
Handling a message read action - Auto sends a read intent based on how your app defined the messaging notification
Handling a reply action - Auto sends a read intent based on how your app defined the messaging notification

## Slide 16: Testing Apps for Auto
Android Auto is available for both car and phone screens
Car screen - Desktop Head Unit (DHU), a testing tool for Auto apps that lets you test pre-released versions of your Android Auto apps
Phone screen - This option lets you display and test pre-released versions of your app on Android Auto for the phone screen
Car screen
DHU enables your development machine to emulate an Android Auto head unit
The DHU runs on Windows, Mac, and Linux hosts
After you’ve installed the DHU, you can test your Android Auto apps by connecting your phone and workstation via USB
Phone screen
Install the Android Auto app, available on Google Play, on your handheld and enable unknown sources in developer mode
Enable USB debugging
Install your app onto the handheld and test

## Slide 17: Auto App Quality
Functionality
Core app quality
Visual Design
  Need to meet all relevant core app quality criteria for the Android platform
  General
  Media
  Notifications
  Messaging
  Driver attention
  Layout
  Visual Contrast
  Interaction
Auto app quality

## Slide 18: Distribute to Android Auto
Understand the guidelines and requirements - read and understand the quality guidelines for Auto apps
Develop a app for Auto - Android Auto is a part of a new or existing app for Android devices, using the same package name and store listing
Test for Auto app quality - Apps should be designed to perform well, look great in the car, and offer the best user experience possible
Agree to Android Auto terms and publish - Google Play submits your app for review against the Auto app quality criteria and notifies you of the result
Track your review
App will be reviewed for compliance with driver distraction guidelines and the technical and quality criteria
After a successful review, your app will be published and made available on the Google Play Store
Notes: https://developer.android.com/distribute/best-practices/launch/distribute-auto.html#how_to_participate

## Slide 19: 4.
Compatible with Android Auto

## Slide 20: Compatible with Android Auto
There are 37 brands of cars that have already implemented Android auto in some models, such as: Audi, Chevrolet, Lamborghini and Volvo
In the near future the Android Auto will be implemented in 16 more brands
Android Auto is also implemented in 5 brands of aftermarket displays, such as: Kenwood, Panasonic and Sony
In the near future Android Auto will be implemented in 4 more brands of aftermarket displays
Android Auto is only available in 31 countries
For Portugal, there isn’t a official release date that, however the APK can be downloaded, and use some functionalities

## Slide 21: 5.
Embedded Android Auto

## Slide 22: Overview – Embedded Android Auto
Release Date: No official release date, shown in May 17, 2017 in Google I/O
Android-based operating system designed for vehicles
Tightly-integrated with the features of the car
  Can control various sensors and switches
Gives the car OEMs more control over the UI
Full customization is important for adoption

## Slide 23: How it works?
Similar to Android Auto
UI elements and built-in apps differ from OEM to OEM
Expect implementations from different automakers to look and feel unique
  Different design elements
  Different display types

## Slide 24: Car Models where it is available (Google I/O 2017)
Audi Q8
Volvo V90 SUVs